## Slide 1: Connecting Renewables Climate Week New York
Patricia Labra
September 2023

## Slide 2
Red Electrica as Spanish TSO: Transmission System Operator
Context National context
SDC –October 2022
System Operator
Guarantees the continuity and security of electricity supply
Sole transmission Agent
Designs, builds and maintains the transmission network and facilitates transmission grid access
Government is responsible of the Energy policy, including the National Development Plan

## Slide 3: Spanish National Energy and Climate Plan (NECP) approved by the Government in 2020
74% of renewables in electricity sector
39,5% of reduction of primary energy consumption
42% of renewables in final energy consumption
Main goal is to reduce greenhouse gas emissions in the Spanish economy by at least 23% by 2030 compared to 1990, by means of …

## Slide 4: Spanish National Energy and Climate Plan (NECP) approved by the Government in 2020
74%81% of renewables in electricity sector
39,5% 44% of reduction of primary energy consumption
42% 48% of renewables in final energy consumption
Main goal is to reduce greenhouse gas emissions in the Spanish economy by at least 23% 32% by 2030 compared to 1990, by means of …
With a proposal of revision in June 2023
Notes: And reduce Energy dependence from 61 to 51%

## Slide 5: Installed Generation Capacity from today to 2030
Installed capacity (31.12.22)
∑ Renewable Capacity ≈ 62,6%
Chart: 
| Wind | Hydraulic | Solar PV | Thermo-solar | Other renewable (*) | Renewable waste | Nuclear | Coal | Combined Cycle | Cogeneration | Non-renewable waste
Serie 1 | 29157 | 17092 | 18691 | 2304 | 1087 | 132 | 7117 | 3223 | 24562 | 5589 | 387
Installed capacity
(Peninsula):
109.341 MW
Peak Demand
38.000 MW
Chart: Installed Capacity 2030
| Nuclear | Carbón | Ciclos | Hidráulica (sin bombeo) | Eólica terrestre | Eólica offshore | Solar FV | Termosolar | Resto RES | Cogeneración y otros | Almacenamiento
 | 0.014931 | 0 | 0.1203 | 0.071504 | 0.28246 | 0.013749 | 0.35724 | 0.023589 | 0.009644 | 0.01999 | 0.086603
∑ Renewable Capacity ≈ 76%
Installed capacity
(Peninsula):
203.649 MW
Peak Demand
51.450 MW
Notes: Sept 2022 Eolica 29700 and solar 22000 ( almost 2,5 GW more)

## Slide 6: Generation Balance from today to 2030
Generation Balance 2022
TOTAL Demand : 235.459 GWh
Chart: 
| Nuclear | Wind | Hydraulic | Cogeneration | Combined Cycle | Solar PV | Coal | Other renewable | Turbinación bombeo | Thermo-solar | Non-renewable waste | Renewable waste
Potencia instalada | 55984 | 59805 | 17860 | 17732 | 60562 | 27283 | 7687 | 4646 | 4123 | 1761 | 739
∑ Renewable energy ≈ 44,3%
∑ Energies with zero CO2 emissions ≈ 66,0 %
Chart: Generation balance 2030
| Nuclear | Carbón | Ciclos | Hidráulica (sin bombeo) | Eólica terrestre | Eólica offshore | Solar FV | Termosolar | Resto RES | Cogeneración y otros
 | 34573.3812 | 0 | 16516.0404 | 28940.5081 | 116970.3809 | 9769.1296 | 127212.3442 | 9469.9926 | 13742.6738 | 19356.4088
TOTAL Demand : 316.5 GWh
∑ Renewable energy ≈ 81%

## Slide 7
3.
Operation – how we succed in integrating >40% RES

## Slide 8: Primary resource variability
monthly average utilization factor
Hourly average utilization factor
Hourly averae utilization factor
Hourly average utilization factor
Hourly average utilization factor
monthly average utilization factor
monthly average utilization factor

## Slide 9: Tool kit in Operation
Forecast
CECRE
SRAP
Provision of services

## Slide 10: Continuous adaptation of the forecast models
10
Forecast
RES Forecast
Demand Forecast
Reduction of error during the last decade
Notes: Self consumption – relevant for demand

## Slide 11: CECRE: Renewable Energy Control Centre
  Pioneer and reference center worldwide in the integration of renewable energies, cogeneration and waste, commissioned in 2006
11
CECRE
Facilities or Agregations
CECRE
P > 5 MW
P > 1 MW
Through a Control Center for Gen&Deman
Through a Control Center for Gen&Deman
  Observability
  Observability & controllability
Manage generation-demand balance
Carry out reliable production forecasts
Manage congestion in the generation evacuation
Minimize generation surpluses that cannot be integrated into the System
Minimize risks to transient stability
Perform network state estimation and congestion analysis

## Slide 12: Automatic Power Reduction System (SRAP)
NUDO 1
NUDO 2
SCADA NUDO 2
SCADA NUDO 1
Scada OS
ICCP 2
Reduction signal
ICCP 1
How does it work?
  Send signals to reduce generation after predefined events in the grid (contingencies).
  New operational tool, integrated in the control system in 2022 that allow to send signals in case of events in the transmisión network: it reduces power plants after N-1 in down to 3 seconds
Reduce needs of RES limitation pre-contingency
More flexibility for the devices to reduce congestions post-contingency
Maximize RES integration and use of the grid
SDC –October 2022
SRAP

## Slide 13: Adaptation of Operational Procedures to RD 413/2014
Possibility of Renewable facilities, after passing enablement tests, to participate in the following ancillary services:
    Replacement Reserves
    Tertiary
    Secondary
Therefore, Renewable facilities are allowed to participate in ancillary services, as long as they pass service-specific prequalification tests
Take the opportunity to integrate RES as an energy with possibilities
Relevant for Demand Coverage
Renewable facilities >= 5 MW must comply with the power factor instructions that the OS defines within the following range::
0.98
1.00
0.98
Capacitive
Inductive
Annex III defines a penalty of 0,261 c€/kWh in case of non-compliance
Future Voltage control: Service providers that will follow real time setpoints (U, Q, power factor)
Participation in Ancillary Services
RD 413/2014: Article 7
Participation in voltage control
Provision of services

## Slide 14
1.
Future challenges and solutions

## Slide 15
System Adequacy
Market curtailments
Capacity Mechanism
Flexibility also for demand  SRAD
Restoration of the system
SDC –October 2022
Generation Adequacy
Demand
Production
Storage
Storage
Network adequacy
Is demand in every hour properly covered ?
Is current network sufficient to accomodate future scenarios of demand and generation?
Technical Curtailments
Technical restrictions
Stability
 Identification of system needs and Solutions

## Slide 16
Network adequacy- Where is the generation located?
Wind Resource Map IDAE
FV Resource Map REE
FV
WInd
Sucess probability index
FV
Wind
RESOURCE MAPS
Environmental zoning for the implementation of RES (MITERD)
FV
Wind
ACCEPTANCE MAPS
STK INTEREST
SDC –October 2022
Wind Expectations x 3 NECP target values
Solar PV Expectations  x 13 NECP target values
Notes: Probability of sucess Maps combine Resource, Efficiency and ease of environmental permitting
Desarrollo de una metodología novedosa basada en pilares de sostenibilidad:
promoción de renovables en base a recurso, primando eficiencia y respeto al medio ambiente
Demanda peninsular:
Valor > en un 4,0 % a la demanda real del año 2019 (valor de 249,1 TWh)
Valor < en un 9% a la demanda central estimada para 2020 en el ejercicio de Planificación 2015-2020. La disminución de demanda prevista a futuro se deriva de las medidas de eficiencia.

## Slide 17: The grid as an enabler of the Energy transision
Balance between a Starting grid & a no limitations grid
17
Starting grid
Starting grid
Curtailment
RES
SDC –October 2022
15%
62%
Curtailment
RES
2,4%
68%
No limitations grid

## Slide 18: The grid as an enabler of the Energy transision
Balance between a Starting grid & a no limitations grid
18
Planned network allows balance among the objectives of the Energy policy, security of supply, economic sustainability and environmental compromise
(*) Coherent with(Art.13.5 Ref(UE) 2016/943
(*)
Starting grid
No limitations grid
Starting grid
Planned grid
System needs identification
Curtailment
Curtailment
Curtailment
Curtailment
RES
RES
RES
RES
SDC –October 2022
15%
2,4%
4% *
62%
68%
68%

## Slide 19
Decision flowchart based on EE1 (energy efficiency principle)
Operational solution
Dynamic Line Rating
Line uprating
Reconductoring
Upgrading
New assets
FACTS
¿Does the solution suit the need? ¿Is it feasible?
Environmental and economic impact
Yes
Yes
Yes
Yes
Yes
Yes
Yes
Included in NDP
Included in NDP
Included in NDP
Included in NDP
Included in NDP
Included in NDP
New operational tools and communications solve 80% of contingency problems
The choice of solutions to solve future network needs prioritise the use of existing network
72 % of actions in the NDP focus on improving and maximising the use of existing lines, that is minimising environmental impact
SDC –October 2022

## Slide 20
Efficiency principle
Operational solution
Dynamic Line Rating
Line uprating
Reconductoring
Upgrading
New assets
FACTS
¿Does the solution suit the need? ¿Is it feasible?
Environmental and economic impact
Yes
Yes
Yes
Yes
Yes
Yes
Yes
Included in NDP
Included in NDP
Included in NDP
Included in NDP
Included in NDP
Included in NDP
New operational tools and communications solve 80% of contingency problems
The choice of solutions to solve future network needs prioritise the use of existing network
72 % of actions in NDP focus on improving and maximising the use of existing lines, that is minimising environmental impact
7.057 km
upratings
722 km
DLR
700 km
renewals
300 km
reconducting
2.681 km
New aerial ROW
734 km
Submarine link
SDC –October 2022

## Slide 21: Toolbox. Tecnological solutions (DLR)
Climate variables
TEMPERATURE
IRRADIANCE
WIND
Static Capacity
Seasonal Capacities
(4 annual values)
Dynamic Capacity
Transmisssion Capacity values computed in real time
722 km
23 lines
DLR allows higher use of existing network in those moments when climate conditions are favorables
SDC –October 2022

## Slide 22: Toolbox. Tecnological solutions (batteries and syncronous condensers)
Submarine HVDC Link (2x200MW)
2 storage systems as fully integrated network elements
(batteries in Mercadal -50MW and San Antonio -90MW)
5 syncronous condensers as fully integrated network elements (in Llubí, Sta Ponsa & Valldurgent)
50 MW
37,5 MWh
90 MW
67,5 MWh
2nd link Spanish Mainland –Balearic Island
SDC –October 2022
Batteries are only prepared for use in case of emergency

## Slide 23: Toolbox. Tecnological solutions
STATCOM
(Moraleja 400kV, Vitoria, Tabernas y Lousame 220kV)
OBJECTIVE: interarea oscillations control
48 reactances (3400Mvar) for voltaje control
Interconections and HVDC
FACTS
3 syncronous condenser in Canary islands
SDC –October 2022
como elementos plenamente integrados en la red de transporte, que permitirán una mejora sustancial en la integración de renovables.

## Slide 24: Strategic Environmental Assessment to asess environmental compatibility
SDC –October 2022
16 MONTHS
25 - 26 MONTHS
TIMELINE NATIONAL DEVELOPMENT PLAN
TIMELINE STRATEGIC ENVIRONMENTAL ASSESSMENT
7.057 km
upratings
722 km
DLR
700 km
renewals
300 km
reconducting
2.681 km
New aerial ROW
734 km
Submarine link
24

## Slide 25: Toolbox of technological solutions
Enlaces en corriente continua
Para el desarrollo interconexiones eléctricas
Automatic Power Reduction System
(SRAP)
To maximize RES integration and use of existing network
Storage as full integrated network element
Power
electronics
To optimize use of submarine links and progress on decarbonization of islands
As static compensators that give robustness to the system
Real Time measure of climatic conditions
To make better use of transmission capacity
Synchonous condenders
HVDC
To integrate more RES and improve the SoS in the islands
Interconnection development
SDC –October 2022

## Slide 26: Network Development Plan 2021-2026
Renewable
integration
Systems interconnection
Economy electrification
Total investment of 7000 M€
International 1260 M€
National 1487 M€
40 %
1549 M€
22 %
1872 M€
27 %
SDC –October 2022

## Slide 27: Global impact of the Network Development Plan 2021-2026
€
67 % RES in the national mix in 2026
Benefits for the society
66 % reduction of CO2eq emissions
Increase of 4.600 M€ in GDP
Support to 78.000 jobs
Savings of 1.600 M€/y in variable generation costs
SDC –October 2022

## Slide 28: Access to the Spanish Network Development Plan
Webpage:
www.planificacionelectrica.es/en
SDC –October 2022

## Slide 29: Conclusions
SDC –October 2022
It is possible to operate a system with a high % of RES although it requires a wide toolkit
Grids are enablers of the energy transition and should be treated like that , and also work on solutions to the barriers for the proper implementation of the right grid at the right moment